## Slide 1
AUTONOMOUS
ARDUINO CAR
PROJECT
The Autonomous Driving System (ADS) is a semester project for the System Engineering & Prototyping module at Hochschule Hamm-Lippstadt. It focuses on developing a robotic vehicle that can follow a line and avoid obstacles autonomously.
HOCHSCHULE
HAMM-LIPPSTADT
Prototyping and Systems Engineering
Amina Boudali · Naved Afridi Rashiq · Tzuen Lin · Farwah Tanseem.

## Slide 2
SYSTEM ENGINEERING
Sensing system: line and obstacle detection
Control system: Arduino decision-making
Motion system: motor driver and DC motors
Power system: battery supply
Mechanical structure: chassis and 3D-printed holders
HOCHSCHULE
HAMM-LIPPSTADT
01
02
03
04
05
ASPECTS

## Slide 3
Design Goal
Balancing printing time, electrical routing, and mechanical stability
Battery Holder
Minimal footprint, saves space for other parts;
let's battery slide in/out easily.
Ultrasonic Sensor Mount
Rock-solid, no wobble; clear sensor eyes for accurate echo/trigger.
Design Approach
HOCHSCHULE
HAMM-LIPPSTADT

## Slide 4
Motor Holder
Height matched to wheels; secure fit prevents motors from falling.
Design Approach
HOCHSCHULE
HAMM-LIPPSTADT
IR Sensor Holder
Adjustable width/height/position for perfect alignment during testing.
Problems we faced many times:
Holder is unable to provide adequate support that allows objects to move freely.

## Slide 5
Hardware Setup & Integration
IR Sensors — Placed Close Together
Ultrasonic — Placed Far Left / Far Right
Design Goal
Optimized sensor performance and system layout for accuracy, reliability, and maintainability.
Narrow sensor spacing enables accurate line-edge detection and rapid path correction.
HOCHSCHULE
HAMM-LIPPSTADT
Wider sensor spacing provides broader obstacle coverage while reducing echo interference.

## Slide 6
Simulation Results
HOCHSCHULE
HAMM-LIPPSTADT
Tinkercad prototype used to test the robot logic
Similar components to the real hardware setup
Some components were replaced due to simulation limits
Helped validate the logic before final code and hardware testing
Tinkercad prototype
Circuit sketch

## Slide 7
Sensor Readings
HOCHSCHULE
HAMM-LIPPSTADT

## Slide 8
Testing Videos
Failure video:
Jerking / unstable correction
Improved video:
Smooth line following
HOCHSCHULE
HAMM-LIPPSTADT
Line Following Logic
Black-line tracking with sensor cases, differential speeds, and memory-based realignment
1
Read sensors
2
Choose case
3 sensor cases
White + White
Line not detected → use memory and search in the last known direction
White + Black / Black + White
One sensor detects the edge → differential speeds curve the car back
Black + Black
Both sensors see the line → keep the car moving stable and straight
i
Extra tuning: the IR potentiometer was adjusted to match the actual line width and surface contrast.
Code Implementation,
Testing and Evaluation
3
Adjust motors
4
Realign
Notes: Presentation script: I am explaining only the line-following logic, not the exact private tuning details. The car follows the black line using two IR sensors. The logic is based on three simple cases. First, white and white means neither sensor sees the black line. In that case, the car uses its last known line position and searches in that same direction to find the line again. Second, white and black, or the mirrored black and white case, means the car is on the edge of the line. Here I correct the direction using differential motor speeds. One motor runs slower and the other runs faster, so the car curves back toward the line instead of making a harsh movement. Third, black and black means both sensors are over the line. The car should stay stable and continue forward. The important recovery part is memory. The car stores where it last saw the black line. If the line is lost, it does not randomly turn; it searches back in the same direction to realign. I also had to adjust the potentiometer on the IR module because the sensor threshold depends on the actual line width and surface contrast. Without this adjustment, the sensor can switch too early or too late, which causes unstable movement. The first video shows the failure case where the car jerks. The second video shows the improved behavior with smoother correction, memory-based recovery, and proper sensor threshold adjustment.

## Slide 9
Testing Videos
Failure video:
Inaccurate avoidance
Improved video:
Smoother rejoin & avoidance
HOCHSCHULE
HAMM-LIPPSTADT
Code Implementation,
Testing and Evaluation
Obstacle Avoidance Logic
Obstacle detection, avoidance sequence, and line recovery using ultrasonic and IR sensor feedback
1
Detect obstacle
2
Stop & confirm
3
Avoid obstacle
4
Recover the line
Obstacle detected → stop and confirm
Avoidance sequence:
Back up → turn away → pass obstacle → realign with line
Main challenge:
The robot had to work at different positions and angles on the track.
Fixes:
Adaptive turn based on ultrasonic readings
IR sensors checked during avoidance
If black line is detected, avoidance stops and line following resumes
Notes: Presentation script: I am explaining only the line-following logic, not the exact private tuning details. The car follows the black line using two IR sensors. The logic is based on three simple cases. First, white and white means neither sensor sees the black line. In that case, the car uses its last known line position and searches in that same direction to find the line again. Second, white and black, or the mirrored black and white case, means the car is on the edge of the line. Here I correct the direction using differential motor speeds. One motor runs slower and the other runs faster, so the car curves back toward the line instead of making a harsh movement. Third, black and black means both sensors are over the line. The car should stay stable and continue forward. The important recovery part is memory. The car stores where it last saw the black line. If the line is lost, it does not randomly turn; it searches back in the same direction to realign. I also had to adjust the potentiometer on the IR module because the sensor threshold depends on the actual line width and surface contrast. Without this adjustment, the sensor can switch too early or too late, which causes unstable movement. The first video shows the failure case where the car jerks. The second video shows the improved behavior with smoother correction, memory-based recovery, and proper sensor threshold adjustment.

## Slide 10
HOCHSCHULE
HAMM-LIPPSTADT
Code Implementation,
Testing and Evaluation
Reverse Logic
01
Memory-based trigger: The code saves when the first obstacle is avoided, so every later obstacle starts the reverse routine.
02
Turn-back sequence: Stop and confirm → back up → slow 180° turn → detect black line.
03
Main challenge: The robot had to rejoin the line without overshooting or missing it.
04
Key fixes: Slower 180° turn, delayed line check, black-line confirmation, and short stabilization before line following resumes.
Testing Video
Reverse test: robot turns back and rejoins the line.​

## Slide 11
THANK YOU FOR JOINING US
HOCHSCHULE
HAMM-LIPPSTADT
Questions?
We are happy to answer any questions about the project.